## Slide 13: INSTRUCTIONS SET OF 8085
DATA TRANSFER GROUP
MOV Rd, Rs.(Move data from Rs to Rd).
Example:
MOV C,B. Move the content of register B to C.
Initially After execution
B=10H. B=10H.
C=20H. C=10H.
Flags Affected :No flags affected.
Addressing mode: Register.

## Slide 14: DATA TRANSFER GROUP
MOV Rd, M (Move data from Memory to Rd).
Example:
MOV C,M. Move the content of Memory i.e. “H or L” to C.
Suppose the Data at memory pointed By HL pair at C200H is 10H.
Initially After execution
H=C2,L=00,C=30H H=C2,L=00,C=10H.
Flags Affected :No flags affected.
Addressing mode: Indirect.

## Slide 15: DATA TRANSFER GROUP
MVI R, Data.(Move Immediate data to Register).
Example:
MVI B, 30H. (Move the data 30 H to Register B)
Initially After execution
B=40H B=30H
Flags Affected :No flags affected.
Addressing mode: Immediate.

## Slide 16: DATA TRANSFER GROUP
LXI Rp,16 bit .(Load 16 bit data to Register pair Immediate).
Example:
LXI SP, C200H. (Load Stack pointer with C200H).
Initially After execution
SP=C800H SP=C200H.
Flags Affected :No flags affected.
Addressing mode: Immediate.

## Slide 17: DATA TRANSFER GROUP
STA address.(Store Acc data to address).
Example:
STA C200H. (Move the data from Acc to C200H).
Suppose in Acc the data is 10H.
Initially After execution
A=10H, C200=20H C200=10H , A=10H
Flags Affected :No flags affected.
Addressing mode: Direct.

## Slide 18: DATA TRANSFER GROUP
LHLD address.(Load HL pair with data from address).
Example:
LHLD C200H. (Move the data from C200 to HL pair).
Suppose at C200 the data is 20H,30H .
Initially After execution
H=10H,L=20H H=20H,L=30H.
C2=20H,00=30H C2=20H,00=30H
Flags Affected :No flags affected.
Addressing mode: Direct.

## Slide 19: DATA TRANSFER GROUP
XCHG (Exchange the data from HL pair to DE pair)
Example : XCHG
Initially After execution
H=20H,L=30H, H=40H,L=70H.
D=40H,E=70H. D=20H,E=30H.
Flags Affected :No flags affected.
Addressing mode: Register.

## Slide 20: DATA TRANSFER GROUP
IN 8 bit address (Move the data from address to Acc)
Example: IN 80H
Move the data from 80H port address to Accumulator.
Suppose data at 80H is 39H.
Initially After execution
A=20H. A=39H
Flags Affected :No flags affected.
Addressing mode: Direct.

## Slide 21: DATA TRANSFER GROUP
OUT 8 bit address (Move the data from Acc to address)
Example: OUT 80H
Move the data from Acc to port address 80H.
Suppose data at Acc is 39H.
Initially After execution
A=39H. 80=10H. A=39H,80=39H.
Flags Affected :No flags affected.
Addressing mode: Direct.

## Slide 22: DATA TRANSFER GROUP
Example:Write a program to exchange contents of memory location D000H to D001H
LDA D000H Load Acc with data from D000
MOV B,A Move the data to B
LDA D0001H Load Acc with data from D001
STA 2000H Store Acc data at D000
MOV A,B Move B’s data to A
STA 2001H Store data from D000 to D0001
RST1 Stop.

## Slide 23: ARITHMETIC GROUP
ADD R (ADD register content with Acc and result in A ).
Example:
ADD C. (ADD the content of C with A).
Suppose the Data at C register is 10H.
Initially After execution
. C= 10H ,A=10H A=20H,C=10H.
Flags Affected :All flags are modified.
Addressing mode: Register

## Slide 24: ARITHMEIC GROUP
ADD M(ADD H or L Reg content with Acc and result in A ).
Example:
ADD M. (ADD the content of HL with A).
Suppose the Data at memory pointed by HL register 1020H is 10H.
Initially After execution
. H= 10H ,L=20H . H=10H,L=20H.
A=20H,C=10H. A=30H.
Flags Affected :All flags are modified.
Addressing mode: Register Indirect.

## Slide 25: ARITHMETIC GROUP
ADI Data(ADD immediate data with Acc and result in A ).
Example:
ADI 30H. (ADD 30H with A).
Initially After execution
A=20H, A=50H.
Flags Affected :All flags are modified.
Addressing mode: Immediate.

## Slide 26: ARITHMETIC GROUP
ADC R (ADD register content with Acc and carry and result in A ).
Example:
ADC C. (ADD the content of C with A with carry).
Suppose the Data at C register is 10H and carry is 01H.
Initially After execution
. C= 10H ,A=10H A=21H,C=10H.
Flags Affected :All flags are modified.
Addressing mode: Register

## Slide 27: ARITHMETIC GROUP
Example: Write a program to perform 16 bit addition of 1234H& 4321H. Store answer at H & L registers.
MVI B,21H B=21H
MVI A,34H A=34H
MVI C,43H C=43H
MVI D,12H D=12H
ADD B A=34+21H
MOV L,A L=55H
MOV A,C A=43H
ADC D A=43+12H
MOV H,A H=55H
RST1 STOP.

## Slide 28: Assembly language program to add two numbers
MVI A, 2H ;Copy value 2H in register A
MVI B, 4H ;Copy value 4H in register B
ADD B ;A = A + B
Note:
Assembly language is specific to a given processor
For e.g. assembly language of 8085 is different than that of Motorola 6800 microprocessor

## Slide 29: 1. Data Transfer (Copy) Operations
  Load a 8-bit number in a Register
  Copy from Register to Register
  Copy between Register and Memory
  Copy between Input/Output Port and Accumulator
  Load a 16-bit number in a Register pair
  Copy between Register pair and Stack memory

## Slide 30: Example Data Transfer (Copy) Operations / Instructions
  Load a 8-bit number 4F in register B
  Copy from Register B to Register A
  Load a 16-bit number 2050 in Register pair HL
  Copy from Register B to Memory Address 2050
  Copy between Input/Output Port and Accumulator
MVI B, 4FH
MOV A,B
LXI H, 2050H
MOV M,B
OUT 01H
IN 07H

## Slide 31: 2. Arithmetic Operations
  Addition of two 8-bit numbers
  Subtraction of two 8-bit numbers
  Increment/ Decrement a 8-bit number

## Slide 32: Example Arithmetic Operations / Instructions
  Add a 8-bit number 32H to Accumulator
  Add contents of Register B to Accumulator
  Subtract a 8-bit number 32H from Accumulator
  Subtract contents of Register C from Accumulator
  Increment the contents of Register D by 1
  Decrement the contents of Register E by 1
ADI 32H
ADD B
SUI 32H
SUB C
INR D
DCR E

## Slide 33: 3. Logical & Bit Manipulation Operations
  AND two 8-bit numbers
  OR two 8-bit numbers
  Exclusive-OR two 8-bit numbers
  Compare two 8-bit numbers
  Complement
  Rotate Left/Right Accumulator bits

## Slide 34: Example Logical & Bit Manipulation Operations / Instructions
  Logically AND Register H with Accumulator
  Logically OR Register L with Accumulator
  Logically XOR Register B with Accumulator
  Compare contents of Register C with Accumulator
  Complement Accumulator
  Rotate Accumulator Left
ANA H
ORA L
XRA B
CMP C
CMA
RAL

## Slide 35: 4. Branching Operations
  These operations are used to control the flow of program execution
  Jumps
    Conditional jumps
    Unconditional jumps
  Call & Return
    Conditional Call & Return
    Unconditional Call & Return

## Slide 36: Example Branching Operations / Instructions
  Jump to a 16-bit Address 2080H if Carry flag is SET
  Unconditional Jump
  Call a subroutine with its 16-bit Address
  Return back from the Call
  Call a subroutine with its 16-bit Address if Carry flag is RESET
  Return if Zero flag is SET
JC 2080H
JMP 2050H
CALL 3050H
RET
CNC 3050H
RZ

## Slide 37: 5. Machine Control Instructions
  These instructions affect the operation of the processor. For e.g.
  HLT Stop program execution
  NOP Do not perform any operation

## Slide 38: 4. Writing a Assembly Language Program
Steps to write a program
  Analyze the problem
  Develop program Logic
  Write an Algorithm
  Make a Flowchart
  Write program Instructions using Assembly language of 8085

## Slide 39: Program 8085 in Assembly language to add two 8-bit numbers and store 8-bit result in register C.
Analyze the problem
  Addition of two 8-bit numbers to be done
Program Logic
  Add two numbers
  Store result in register C
  Example
  10011001 (99H) A
  +00111001 (39H) D
  11010010 (D2H) C

## Slide 40: 3. Algorithm
Get two numbers
Add them
Store result
Stop
Load 1st no. in register D
Load 2nd no. in register E
Translation to 8085 operations
Copy register D to A
Add register E to A
Copy A to register C
Stop processing

## Slide 41: 4. Make a Flowchart
Start
Load Registers D, E
Copy D to A
Add A and E
Copy A to C
Stop
Load 1st no. in register D
Load 2nd no. in register E
Copy register D to A
Add register E to A
Copy A to register C
Stop processing

## Slide 42: 5. Assembly Language Program
Get two numbers
Add them
Store result
Stop
Load 1st no. in register D
Load 2nd no. in register E
Copy register D to A
Add register E to A
Copy A to register C
Stop processing
MVI D, 2H
MVI E, 3H
MOV A, D
ADD E
MOV C, A
HLT

## Slide 43: Program 8085 in Assembly language to add two 8-bit numbers. Result can be more than 8-bits.
Analyze the problem
  Result of addition of two 8-bit numbers can be 9-bit
  Example
  10011001 (99H) A
  +10011001 (99H) B
  100110010 (132H)
  The 9th bit in the result is called CARRY bit.

## Slide 44
0
How 8085 does it?
  Adds register A and B
  Stores 8-bit result in A
  SETS carry flag (CY) to indicate carry bit
10011001
10011001
A
B
+
99H
99H
10011001
A
1
CY
00110010
99H
32H

## Slide 45
Storing result in Register memory
10011001
A
32H
1
CY
Register C
Register B
Step-1 Copy A to C
Step-2
  Clear register B
  Increment B by 1

## Slide 46: 2. Program Logic
Add two numbers
Copy 8-bit result in A to C
If CARRY is generated
  Handle it
Result is in register pair BC

## Slide 47: 3. Algorithm
Load two numbers in registers D, E
Add them
Store 8 bit result in C
Check CARRY flag
If CARRY flag is SET
  Store CARRY in register B
Stop
Load registers D, E
Translation to 8085 operations
Copy register D to A
Add register E to A
Copy A to register C
Stop processing
Use Conditional Jump instructions
Clear register B
Increment B
Copy A to register C

## Slide 48: 4. Make a Flowchart
Start
Load Registers D, E
Copy D to A
Add A and E
Copy A to C
Stop
If
CARRY
NOT SET
Clear B
Increment B
False
True

## Slide 49: 5. Assembly Language Program
MVI D, 2H
MVI E, 3H
MOV A, D
ADD E
MOV C, A
HLT
Load registers D, E
Copy register D to A
Add register E to A
Copy A to register C
Stop processing
Use Conditional Jump instructions
Clear register B
Increment B
Copy A to register C
JNC END
MVI B, 0H
INR B
END:

## Slide 50: 4. Addressing Modes of 8085
Format of a typical Assembly language instruction is given below-
[Label:] Mnemonic [Operands] [;comments]
HLT
MVI A, 20H
MOV M, A ;Copy A to memory location whose address is stored in register pair HL
LOAD: LDA 2050H ;Load A with contents of memory location with address 2050H
READ: IN 07H ;Read data from Input port with address 07H

## Slide 51
The various formats of specifying operands are called addressing modes
Addressing modes of 8085
  Register Addressing
  Immediate Addressing
  Memory Addressing
  Input/Output Addressing

## Slide 52: 1. Register Addressing
Operands are one of the internal registers of 8085
Examples-
MOV A, B
ADD C

## Slide 53: 2. Immediate Addressing
Value of the operand is given in the instruction itself
Example-
MVI A, 20H
LXI H, 2050H
ADI 30H
SUI 10H

## Slide 54: 3. Memory Addressing
One of the operands is a memory location
Depending on how address of memory location is specified, memory addressing is of two types
  Direct addressing
  Indirect addressing

## Slide 55: 3(a) Direct Addressing
16-bit Address of the memory location is specified in the instruction directly
Examples-
LDA 2050H ;load A with contents of memory location with address 2050H
STA 3050H ;store A with contents of memory location with address 3050H

## Slide 56: 3(b) Indirect Addressing
A memory pointer register is used to store the address of the memory location
Example-
MOV M, A ;copy register A to memory location whose address is stored in register pair HL
30H
A
20H
H
50H
L
30H
2050H

## Slide 57: 4. Input/Output Addressing
8-bit address of the port is directly specified in the instruction
Examples-
IN 07H
OUT 21H

## Slide 58: 5. Instruction & Data Formats
8085 Instruction set can be classified according to size (in bytes) as
  1-byte Instructions
  2-byte Instructions
  3-byte Instructions